## Slide 1: Module 8.3 – Parallel Computation Patterns (Stencil)
Tile Boundary Conditions

## Slide 2: Objective
To learn to write a 2D convolution kernel
  2D Image data types and API functions
  Using constant caching
  Input tiles vs. output tiles in 2D
  Thread to data index mapping
  Handling boundary conditions

## Slide 3: 2D Image Matrix with Automated Padding
It is sometimes desirable to pad each row of a 2D matrix to multiples of DRAM bursts
  So each row starts at the DRAM burst boundary
  Effectively adding columns
  This is usually done automatically by matrix allocation function
  Pitch can be different for different hardware
Example: a 3X3 matrix padded into a 3X4 matrix
M0,1
M0,0
M1,0
M0,2
M1,1
M2,0
M2,2
M2,1
M1,2
height
width
pitch
Padded
elements
Height is 3
Width is 3
Channels is 1 (See MP Description)
Pitch is 4
3

## Slide 4: Row-Major Layout with Pitch
M0,2
M1,1
M0,1
M0,0
M1,0
M1,2
M0,2
M0,1
M0,0
M1,1
M1,0
M1,2
M2,1
M2,0
M2,2
M2,1
M2,0
M2,2
M
Row*Pitch+Col = 2*4+1 = 9
M2
M1
M0
M3
M5
M4
M6
M7
M9
M8
M10
M11
M
Padded elements

## Slide 5: Image Matrix Type in this Course
// Image Matrix Structure declaration
//
typedef struct {
int width;
int height;
int pitch;
int channels;
float* data;
} * wbImage_t;
This type will only be used in the host code of the MP.

## Slide 6: wbImage_t API Function for Your Lab
wbImage_t wbImage_new(int height, int width, int channels)
wbImage_t wbImport(char * File);
void wbImage_delete(wbImage_t img)
int wbImage_getWidth(wbImage_t img)
int wbImage_getHeight(wbImage_t img)
int wbImage_getChannels(wbImage_t img)
int wbImage_getPitch(wbImage_t img)
float *wbImage_getData(wbImage_t img)
For simplicity, the pitch of all matrices are set to be
width * channels (no padding) for our labs.
The use of all API functions has been done in the provided host code.

## Slide 7: Setting Block Size
#define O_TILE_WIDTH 12
#define BLOCK_WIDTH (O_TILE_WIDTH + 4)
dim3 dimBlock(BLOCK_WIDTH,BLOCK_WIDTH);
dim3 dimGrid((wbImage_getWidth(N)-1)/O_TILE_WIDTH+1, (wbImage_getHeight(N)-1)/O_TILE_WIDTH+1, 1)
In general, BLOCK_WIDTH should be
O_TILE_WIDTH + (MASK_WIDTH-1)

## Slide 8: Using constant memory and caching for Mask
Mask is used by all threads but not modified in the convolution kernel
  All threads in a warp access the same locations at each point in time
CUDA devices provide constant memory whose contents are aggressively cached
  Cached values are broadcast to all threads in a warp
  Effectively magnifies memory bandwidth without consuming shared memory
Use of const __restrict__ qualifiers for the mask parameter informs the compiler that it is eligible for constant caching, for example:
__global__ void convolution_2D_kernel(float *P,
float *N, height, width, channels,
const float __restrict__ *M) {

## Slide 9: Shifting from output coordinates to input coordinate
int tx = threadIdx.x;
int ty = threadIdx.y;
int row_o = blockIdx.y*O_TILE_WIDTH + ty;
int col_o = blockIdx.x*O_TILE_WIDTH + tx;
int row_i = row_o - 2;
int col_i = col_o - 2;
row_o for
Thread (0,0)
row_i for
Thread (0,0)

## Slide 10: Taking Care of Boundaries (1 channel example)
if((row_i >= 0) && (row_i < height) &&
(col_i >= 0) && (col_i < width)) {
Ns[ty][tx] = data[row_i * width + col_i];
} else{
Ns[ty][tx] = 0.0f;
}
Use of width here is OK since pitch is set to width for this MP.

## Slide 11: Some threads do not participate in calculating output. (1 channel example)
float output = 0.0f;
if(ty < O_TILE_WIDTH && tx < O_TILE_WIDTH){
for(i = 0; i < MASK_WIDTH; i++) {
for(j = 0; j < MASK_WIDTH; j++) {
output += M[i][j] * Ns[i+ty][j+tx];
}
}

## Slide 12: Some threads do not write output (1 channel example)
if(row_o < height && col_o < width)
data[row_o*width + col_o] = output;
You need to write the kernel for a 3-channel (RGB) image.
See more details in the Lab MP Description.

## Slide 13
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.